## Slide 1: Three-component spatial autocorrelation processing using SeisImager modules
Processing ambient noise data obtained by Atom 3C and/or MT-Neo.
SeisImager/SW3C license is required.
Download the latest installer from : http://seisimager.com/download/SeisImager.zip
Y(NS)
X(EW)

## Slide 2: Outline of three-component (3C) measurement and processing
Y(NS)
X(EW)
Z(UD)
3C measurement
3C ambient noise data
X(EW)
Y(NS)
Z(UD)
3C spatial autocorrelation
Radial
Transverse
Vertical
Rayleigh and Love wave dispersion curves
Rayleigh
Love
S-wave velocity model
3C measurement provides 3C ambient noise data.
Vertical component provides vertical component SPAC. Horizontal components (X and Y) provide radial and transverse component SPACs.
Vertical component SPAC provides a Rayleigh dispersion curve. Horizontal components (radial and transverse) provide a Love dispersion curve using Rayleigh dispersion curve.
Joint inversion of Rayleigh and Love dispersion curves provide an S-wave velocity model.

## Slide 3: 3C ambient noise measurements for SPAC
Triangular array (T4)
L-shaped array (L3)
Arrange the orientation of all sensors to be the same direction

## Slide 4: Spatial autocorrelation for 3C ambient noise
Radial component
Radial component
Transverse component
Transverse component
Radial and transverse components are defined for each receiver pair.
A function calculating transpose and radial components of SPAC from 3C ambient noise data was implemented in SPACPlus and dPickwin.
Direction of horizontal components must be consistent throughout all sensors and kept track.
X(EW)
component
Y(NS)
component
X(EW)
component
Y(NS)
component
Rotate horizontal components (X and Y) to radial and transpose components

## Slide 5: SW3C option in SeisImager
“SW3C option” should be checked in SeisImagerRegistarioan to use 3C processing functions or joint inversion of Rayleigh and Love waves.

## Slide 6: Select a CTB including 3C ambient noise data
Example of three component data

## Slide 7: Data example (3C measurements using 14 sensors)
Easting [m] | Northing [m]
0 | 0
217.34 | 302.07
386.02 | 14.16
-257.41 | -166.41
-362.36 | 182.01
-77.33 | 408.01
120.86 | -76.71
129.83 | 31.65
-96.66 | -105.19
38.67 | 132.35
-83.89 | 112.35
256.12 | -315.96
-91.77 | -381.87
25.57 | -134.09

## Slide 8: 3C SPAC processing flow using SPACPlus, Pickwin and WaveEq
3C CTB
SPAC (vertical)
SPAC (radial)
SPAC (transverse)
SEG2 file (.coh)
SEG2 file (.coh)
SEG2 file (.coh)
3C SPAC
Rayleigh phase velocity image
Love phase velocity image
Rayleigh dispersion curve
Love dispersion curve
SPACPlus
Pickwin
WaveEq

## Slide 9: CTB including 3C ambient noise data by 14 sensors

## Slide 10: Calculate SPAC for each component
Click to calculate SPAC
Select a component to be calculated (selecting vertical component)
Select array geometry. Click “Open array file” if manual array file will be used.
Select “Manual array” if manual array will be used.
Click “OK” to calculate SPAC.

## Slide 11: Individual SPAC for each receiver spacing

## Slide 12: Calculate dispersion curve for each component
Click to calculate dispersion curve
Vertical component
Dispersion curve from vertical component corresponds to Rayleigh wave dispersion curve.

## Slide 13: Save coherencies of each component to a SEG2 file
Select “File”, “Save SPAC data as SEG2 file” to coherencies to a SEG2 file.
Use extension “.coh” to save coherencies.

## Slide 14: Repeat SPAC calculation for all components
Radial component
Transpose component
Note that dispersion curves from transverse and radial components do not correspond to Love wave dispersion curve.

## Slide 15: Switch Pickwin to the complete menu
Use the “Complete menu” to process 3C SPAC data.
Select “Option”, “Menu type”, “Simple” to the menu type from “Simple” to “Complete”.
Complete menu
Simple menu

## Slide 16: Import three SPAC files to Pickwin
Select “File”, “Option”, “Append files” to import multi files at once.
Select three coherency files (vertical, radial and transverse) and click “Open”.

## Slide 17: Import three SPAC files to Pickwin
Click “Yes” to continue.
Three component (vertical, radial and transverse) SPACs appear.

## Slide 18: Calculate Rayleigh and Love phase velocity images
Click or press “Ctrl+D”
to calculate phase velocity images.
Click “Yes” to apply 3C SPAC analysis.
Set up transformation parameters as usual.

## Slide 19: Calculate Rayleigh and Love phase velocity images
Ryleigh wave phase velocity image appears at first.
Click to switch Rayleigh/Love phase velocity images.
Rayleigh wave
Love wave
Note that the color scale of Love wave phase velocity image is opposite to Rayleigh wave.

## Slide 20: Show Rayleigh and Love dispersion curves by WaveEq
Click or select “Surface wave analysis”, “Show phase velocity curve (1D)” to show dispersion curves by WaveEq.
WaveEq launched and Rayleigh wave dispersion curve appears at first.
Click to show Love wave dispersion curve.
Rayleigh
Love

## Slide 21: Edit dispersion curve and prepare an initial model
Edit dispersion curves and prepare an initial model as usual.
Comparison of observed and theoretical dispersion curves (fundamental mode).
Rayleigh
Love
Observed
Theoretical

## Slide 22: Comparison of observed and theoretical dispersion curves (Higher modes)
Rayleigh
Love
Observed
Fundamental
Averaged
(effective)
Velocity
Amplitude
Velocity
Amplitude
1st
2nd
3rd
4th
5th

## Slide 23: Joint inversion of Rayleigh and Love waves
Joint inversion of Rayleigh and Love waves using non-linear least squares method or Genetic Algorithm (GA) were implemented in WaveEq.
Inversions are available in “Inversion (LSM)”, “GA (Vs only)” and “GA (Vs and thickness)” in “MASW/MAM (1D)” of WaveEq.

## Slide 24: Joint inversion of Rayleigh and Love waves
True velocity model
Theoretical velocity model for the true velocity model
Both Rayleigh and Love wave effective modes are different from fundamental modes.
Numerical example using two layer model

## Slide 25: Joint inversion of Rayleigh and Love waves (only fundamental mode)
Initial model
Inverted result
Inversion using non-linear least squares method.
Inversion using non-linear least squares method decreased the error between observed and theoretical dispersion curves.

## Slide 26: Joint inversion of Rayleigh and Love waves (including higher modes)
Initial model
Inverted result
Inversion using Genetic Algorithm (GA).
Inversion using GA decreased the error between observed and theoretical (effective mode) dispersion curves.

## Slide 27: Joint inversion of Rayleigh and Love waves (including higher modes)
Initial model
Inverted result
Inversion using Genetic Algorithm (GA).
Field data example

## Slide 28: Option : Use dispersion curve from transverse component as Love wave
3C spatial autocorrelation
Transverse (or SH measurement)
Vertical
(or P-Sv measurement)
Rayleigh and Love wave dispersion curves
Rayleigh
Love
S-wave velocity model
Theoretically, phase velocities of transverse component is close to that of Love waves. You may consider dispersion curve of transverse component as that of Love waves. In active methods, dispersion curves obtained from SH measurements can be considered as the dispersion curves of Love waves.
Love wave .rst file
Rayleigh wave .rst file

## Slide 29: Option : Select Rayleigh or Love dispersion curve
You have a chance to select Rayleigh or Love dispersion curve
when launching WaveEq from Pickwin.
Rayleigh wave is shown as red
Love wave is shown as blue

## Slide 30: Option : Switch Rayleigh or Love dispersion curve
It is possible to switch (or select) Rayleigh or Love dispersion curve.
Use “MASW/MAM (1D)”, “Advanced option”, “Surface wave mode”.
Rayleigh wave is shown as red
Love wave is shown as blue

## Slide 31: Option : Combine Rayleigh and Love dispersion curves
1) Save Rayleigh and Love wave dispersion curves to individual files.
2) Open one (Rayleigh/Love) file.
3) Open another (Love/ Rayleigh) file and append it.
4) Select “Yes”.
5) Rayleigh and Love dispersion curves are shown together.